## Slide 1: Nat5 design & Manufacture
Woodturning Lathe

## Slide 2: Learning intentions & success criteria
Learning Intentions
Overview of the woodturning lathe, its safety practices, tools and processes.
Success Criteria
State the safe working practices when using a woodturning lathe.
Name and describe the components, tools and processes in the use of the woodturning lathe.

## Slide 3: What is a woodturning lathe?
The woodturning lathe is a machine tool used with hand held tools to shape a piece of wood symmetrically around a central axis of rotation.
Example of products could include: stair spindles, baseball bats, bowls etc.

## Slide 4: ?
?
On/Off Switch
Speed Control
Headstock
Forked Centre
Tool Rest
Bed
Revolving Centre
Tailstock
Tool Post
Faceplate
Parts of a Woodturning Lathe

## Slide 5: ?
?
When turning between centres, the work piece is held between a Forked Centre and a Revolving Centre

## Slide 6: ?
?
Headstock
This supports one end of the work piece.
It contains the driveshaft as shown below.

## Slide 7
The Headstock can be fitted with a Forked Centre to support one end of the work piece when turning between centres.
Forked Centre

## Slide 8
The Headstock can be fitted with a Butterfly Centre to support one end of the work piece when turning between centres.
This provides a greater grip that a forked centre.
Butterfly Centre

## Slide 9
Tailstock
Tailstock Locking Lever
The tailstock supports the other end of the work piece.
Hand Wheel
Bed

## Slide 10
Revolving Centre
Dead Centre
Revolves as the wood turns.
Remains fixed, therefore friction may occur. Use wax to lubricate the centre.

## Slide 11: Woodturning tools
Wood turning tools are used to shape the work piece.
Depending on what shape is required will ultimately determine what type of tool will be used.
The tool rest is used to support the tools while shaping is being carried out.

## Slide 12: GOuge
The Gouge utilises a slicing action and can be used for both roughing down and fine finishing.
Cross Section

## Slide 13: Parting chisel
The parting tool can be used to cut narrow slots in your work piece. It creates a gap in the wood and is used to cut off a section of the wood to an exact length (part off).

## Slide 14: Skew chisel
The skew chisel can be used to produce a very smooth finish. They are basic chisels used in spindle turning for cutting beads, shearing the ends of boxes or cylinders and smoother the edges.

## Slide 15: scraper
Scrapers are among the easiest lathe tools to use however as the name suggests the tool scrapes rather than cuts and can leave a rather rough finish.
Scrapers are available in a wide range of shapes and sizes.

## Slide 16: faceplate
A Faceplate is used to attach a wood blank to the lathe when making, for example, a bowl.

## Slide 17: Outside callipers
The callipers are used to check the outside diameter of various objects.
Once set, the size between each leg can be read using a steel rule.

## Slide 18: Preparing a blank for turning
The wood lathe is a machine used to create cylindrical objects in wood, i.e. wooden bowls, table legs, etc.
A piece of wood is secured between two points called the HEADSTOCK and the TAILSTOCK.
The HEADSTOCK has a motor
enclosed and is therefore the end which actually turns the wood.
The surface finish of the wood being turned can be improved by increasing the speed of the lathe.

## Slide 19: Preparing a length of wood for turning
Use Tenon Saw to cut a diagonal groove to one end of the piece of wood. This helps the centre prongs to grip the piece of wood
The drive centre is hammered into position at the grooved end using a mallet
Remove waste wood using suitable plane
1.
Using compass, draw circle to mark in shape
2.
3.
4.
5.
6.

## Slide 20: Marking out and turning
After preparing the wood for turning, there are a number of processes to be carried out to make your final product (e.g. the coat pegs you have been working on).

## Slide 21: Use the roughing gouge to turn the wood into a cylinder

## Slide 22: Reduce diameter required for your piece

## Slide 23: Mark out features on wood using a pencil and steel rule
Ensure there is sufficient waste wood near centres

## Slide 24: When complete, ensure a smooth surface with sand paper

## Slide 25: For additional smoothness, use leftover shavings. This is called “burnishing.”

## Slide 26: Add varnish, wax or other finished to the wood whilst it is still on the lathe

## Slide 27: Remove the pieces using the parting chisel, skew chisel or sawing

## Slide 28: safety
?
https://www.youtube.com/watch?v=IiLNIM3JUlg

## Slide 29: Personal safety
There are a number of safety checks to be carried out, both on the wood lathe itself and personal safety checks.
What PERSONAL safety checks should you carry out before working on the wood lathe?
Wear a face shield/goggles
No loose clothing/hair
Ensure extraction is on
Hold the tools correctly
Remove debris regularly
Hands clear of faceplate/centres

## Slide 30: MACHINE safety
What MACHINE safety checks should you carry out before working on the wood lathe?

## Slide 31: Wood is securely attached to centres

## Slide 32: Small a gap as possible between wood and tool rest

## Slide 33: Chisels are kept sharp to ensure a good cut and to avoid accidents

## Slide 34: Tool rest centrally aligned with work piece

## Slide 35: Nothing should be left on the lathe bed

## Slide 36: Waste Extraction should be in position

## Slide 37: Tool rest and tail stock should be locked in position